## Slide 1: Embedded Systems Security
Brought to you by Whitescope
contact@whitescope.io
Version: 0.1B

## Slide 2: Thanks
Content Development/Review:
Terry McCorkle
Jonathan Butts
Admin/Logistics:
Charles Warloe (licensing discussion)
Jose Granado, my first infosec mentor, RIP

## Slide 3: Thanks
To the members of information security community, who provided me with the opportunity and support to learn about cybersecurity. I can never fully pay back everything that was given to me, but I hope you will accept this as a token of my gratitude for every thing you’ve helped me with.
Thank you!

## Slide 4: About:This Course
This course is intended to be a foundational course for embedded device security. The labs are designed to provide a repeatable, low cost approach to learning embedded device security fundamentals.
This material will be periodically updated and is maintained here:
https://github.com/bkrios/Embedded-Device-Security-Training/

## Slide 5: About:Whitescope
Embedded device security consulting
Software solutions for Building Control security
Hands on experience with:
  Aviation security
  DoD weapon systems
  Automobile cyber security
  Locomotive cyber security
  Sporting stadiums / event cyber security
  Building Automation/Control

## Slide 6: About:Author
Billy Kim Rios
Founder

## Slide 7: Understanding the License
This course is licensed under as:
Creative Commons – Attribution + Noncommercial (BY-NC)
If you’d like to teach this course WITHOUT charging a fee, please grab the slides and instructor materials from the Github.
If you’re going to charge students/customers for activities utilizing these materials, you’ll need to purchase a license. Contact us at:
training@whitescope.io

## Slide 8: Agenda
TDB

## Slide 9: Examples of Embedded Systems

## Slide 10: These are Embedded Systems Too

## Slide 11: These are Embedded Systems Too

## Slide 12: Traditional IT Systems
Confidentiality
Integrity__
Availability
Focused on data
Protecting business
Protecting brand

## Slide 13: Embedded Systems
Safety
Patient Harm
Fire Hazard
Over Pressure
Targeting Miss
Unauthorized Launch
Unauthorized Jettison
Misdiagnosis
Striking Hazard
Proportionality Miss
Explosion Hazard
Manufacturing Defect

## Slide 14: Embedded Device Security Challenges
Fragmentation makes scaling defense difficult
Customized/proprietary hardware needed for analysis
Constraints on hardware make “extras” hard to implement
Instrumentation can be difficult, especially for automation
Attackers may have physical access to the device
Training hasn’t matured like other cybersecurity areas
Regulatory requirements can introduce additional complexity

## Slide 15: Embedded Systems – Owner
Has ownership of the system
Can establish contractual obligations for manufacturers
Should work closely with operators to understand requirements
Should work closely with manufacturers and integrators
Can be different from the operator of the system (ex. comm air)
May be liable for actions arising from the system

## Slide 16: Embedded Systems – Operator
Operates the system
Typically has the most interaction with the system
Usually has the deepest understanding of system capabilities
May not understand the technical details associated with components
Can also be the owner, but not usually the case with complex systems
May have liability for effects resulting from system activities

## Slide 17: Embedded Systems – Manufacturer
Builds the components within a system
Components may be custom built or off the shelf
Usually responsible for updating software/firmware on components
Should have the deepest understanding of tech details of systems
May also act as a system integrator or a maintainer

## Slide 18: Embedded Systems - Integrators
System integrators typically provide subject matter expertise
Assist in the implementation/deployment of complex systems
Have a hand in developing deployment architectures
Can assist/direct the selection of technologies and components
May also act as a maintainer or even as an owner/operator

## Slide 19: Embedded Systems - Maintainers
Provide support activities to keep the system running
Typically has privileged access to the various system components
Normally has the ability to query components and collect data
Access to maintenance tools and software
Typically has deep, technical knowledge of system components
Can also be a system integrator

## Slide 20: Embedded Systems - Components

## Slide 21: Microprocessors
Processing unit, typically on a standalone integrated circuit
Typically does not have built in RAM/ROM/peripherals
Typically does not have other peripherals built in
May be more suitable for general purpose computing

## Slide 22: Microprocessors

## Slide 23: Microcontrollers or System on Chip (SOC)
Can contain a microprocessor
Typically contains the peripherals required to run applications
May be more appropriate for special purpose systems
Can include peripherals like:
  Graphics Processing Unit
  Global Positioning System
  USB support
  WiFi or cellular support

## Slide 24: Microcontrollers or System on Chip (SOC)

## Slide 25: x86
Originally named after the instruction set used on 8086 processors
Now refers to 32bit instruction set compatible with Intel’s 386
x86 utilizes a variable instruction length
Based on Complex Instruction Set Computing (CISC)
Very common in general computing devices
Less common in embedded systems, but they do exist

## Slide 26: ARM
Advanced RISC Machine
Based on Reduced Instruction Set Computing (RISC)
ARM Holdings (SoftBank Group) develops and licenses ARM
Various companies license ARM and produce their own products
Supports 32-bit instruction sets (some support 16-bit instructions)
Extremely common in embedded devices

## Slide 27: RISC
RISC based architectures utilizes fewer transistors than CISC
Fewer transistors translates into lower costs and power requirements
Utilizes a (relatively) small, highly optimized set of instructions
Processor cycles required to execute a single instruction is “reduced”
Utilizes a load and store architecture
Logic and arithmetic instructions operate only on CPU registers

## Slide 28: PowerPC (PPC)
Created in 1991 by the Apple, IBM, Motorola alliance (AIM)
Utilizes a RISC instruction set architecture
Based on the POWER instruction set (POWER ISA in newer chips)
32-bit and 64-bit implementations
Can switch endianness through the Machine State Register
Used in automobiles and avionics

## Slide 29: MIPS
Created in 1981 at Stanford University
Utilizes a RISC instruction set architecture
Based on the MIPS instruction set
Load and Store architecture
32-bit and 64-bit variants are available

## Slide 30: Field-Programmable Gate Array (FPGA)
First FPGA was created in 1985 by Ross Freeman
Integrated circuit containing programmable logic block
Designed to be configured after production manufacturing
Some FPGAs contain built-in memory components
Configuration must be reloaded when power is applied/re-applied
Advantages: Speed, reliability and flexibility
Disadvantages: Lack of support and high complexity

## Slide 31: Field-Programmable Gate Array (FPGA)

## Slide 32: Complex Programmable Logic Device (CPLD)
EEPROM based
Offers persistence through design locking
Smaller gate count and logic block size when compared with FGPAs
Often used for “simple” logic
Can be faster and more predictable than FPGAs
Usually cheaper than FPGAs, however not as capable

## Slide 33: Complex Programmable Logic Device (CPLD)

## Slide 34: Chip Packaging

## Slide 35: Through-hole Package
Pins for the chips go through the board
Chips are soldered to the underside of the board
Chips are easily removed and replaced
Common in both older and newer chips
External devices can be affixed to the chip

## Slide 36: Surface Mount
Chips are affixed to the surface of the board
Each IC leg is soldered to an individual pad
Chips can be removed with little trouble
Chips can be replaced onto original pads
Chips can have affixed, external devices directly to the chip

## Slide 37: Quad Flat Package
Considered surface mount package
Usually a square chip
Contains pins on each of the four sides
Pin spacing can make soldering more difficult
Multiple variants of QFP (ex. BQFP, TQFP)

## Slide 38: Chip Carrier
Considered surface mount package
Designed to allow for quick removal
Chips are easily replaced
Chips are extracted via chip extractor
Attaching an external device is trivial
Common for ROM as swapping requires low effort

## Slide 39: Pin Grid Array
Common amongst processors
Utilizes a “grid” of pins on the underside
In many cases, the chip is removable
In many cases, the chip can be replaced
External devices can be affixed

## Slide 40: Thin Small Outline Package
Commonly referred to as TSOP
Considered a surface mount package
Frequently used for RAM or Flash
## in TSOP## indicates number of pins

## Slide 41: Ball Grid Array
Considered surface mount package
Connections to pads via conductive balls
Connections obscured
Specialized equipment for removal
Common in newer microprocessors/microcontrollers
Pins over the entire surface area = more pins

## Slide 42: Random Access Memory (RAM)
Sometimes referred to as volatile memory
Utilized when power is applied to the chip
Contents are typically not available on powered off chips
Software and data stored on RAM
Sensitive data is can stored within RAM (passwords, keys)

## Slide 43: Read Only Memory (ROM)
Typically offers a persistent means to store applications/data
Applications/data on ROM should survive a power cycle
Contents burned to chip at manufacture time
Some chips offer a capability to erase and re-program
Typically stores a firmware image that is loaded to RAM
Can store the bootloader

## Slide 44: Communication Buses
Provides the paths for various components to communicate
Ex. Processor utilizing data from RAM
If the bus is exposed, it can be tapped
Buses can reside between PCB layers making it more difficult to tap

## Slide 45: Embedded Systems Architectures

## Slide 46: Embedded Systems - Hardware
Goals

## Slide 47: Embedded Systems - Software
Goals

## Slide 48: Embedded Systems - Firmware
Firmware is actually software
Contains the logic to operate the embedded devices
Typically contains the logic to initiate physical effects
Usually loaded on non-volatile memory (ROM, EPROM, flash)
Some firmware is permanent and cannot be updated
Most newer devices provide a path update firmware

## Slide 49: Bootloaders
Software that loads follow-on software on the embedded system
Usually small in size
Typically loads and initializes the operating system on the device
Can provide a mechanism for recovery if an OS failure occurs
Some systems do not utilize a bootloaders
Some systems boot directly into an application program

## Slide 50: Bootloaders
Flash EEPROM
Bootloader
Firmware 1
(typically compressed)
Firmware 2
(typically compressed)

## Slide 51: Bootloaders
Flash EEPROM
Bootloader
Firmware 1
Firmware 2
DRAM
Reset Vector

## Slide 52: Bootloaders
Flash EEPROM
Bootloader
Firmware 1
Firmware 2
DRAM
Initialize DRAM

## Slide 53: Bootloaders
Flash EEPROM
Bootloader
Firmware 1
Firmware 2
DRAM
Execute Firmware1

## Slide 54: Bootloaders
Flash EEPROM
Bootloader
Firmware 1
Firmware 2
DRAM
Real Time OS
Decompression

## Slide 55: Bootloaders
Flash EEPROM
Bootloader
Firmware 1
Firmware 2
DRAM
Real Time OS
Switch from Flash execution to DRAM

## Slide 56: Bootloaders
Flash EEPROM
Bootloader
Firmware 1
Firmware 2
DRAM
Real Time OS
Temp Storage
DRAM Execution

## Slide 57: Firmware Update
Flash EEPROM
Bootloader
Firmware 1
(typically compressed)
Firmware 2
(typically compressed)

## Slide 58: Real Time Operating Systems
Many embedded devices utilize Real Time Operating Systems (RTOS)
RTOS can look/feel like traditional operating systems
RTOS do implement more controlled/defined scheduling
Many include watchdog components to increase reliability
Some RTOS are “certified” (ex. Greenhills Integrity)
Applications usually run with high privileges

## Slide 59: VxWorks
Common RTOS found in a variety of systems
Developed by Wind River in 1987
Supports MIPS, x86, PPC, and ARM
User-mode apps serperated
Used in the Mars Rover and other devices

## Slide 60: BusyBox
A RTOS built specifically for embedded devices in 1999
“The swiss army knife of Embedded Linux”
Very popular amongst embedded devices
A single executable that provides a number of stripped down tools
Single binary reduces overhead
Single binary allows code to be shared between multiple apps
Released as free software under GNU General Public

## Slide 61: QNX
RTOS originally developed in 1982 by Quantum Software Systems
One of the first commercially successful microkernel OS
Supports MIPS, PPC, x86, and ARM
Unix like OS with GUI and shell
Older systems can be deployed on a FD
Used in automotive telematic systems

## Slide 62: Android
Bought by Google in 2005 and released in 2007
Based on the Linux Kernel
Auto version for automotive, Wear version for wearables
Runs a variety of mobile devices, tablets, and notebooks
Primary interface based on gestures (touch, swipe…etc.)
Apps written in Java with unmanaged (C/C++) libraries

## Slide 63: IOS
Mobile Operating System created by Apple in 2007
Primary interface based on gestures (touch, swipe…etc.)
Native applications written in Swift, Objective-C, C, C++
Applications are served via the Apple App Store
Based on the XNU operating system (X is not Unix)
Hybrid kernel based on the Mach Kernel and BSD

## Slide 64: Integrity
Developed by Greenhills and released in 2008 (commercial)
First system to be certified by NIAP to EAL-6
POSIX based RTOS
User/Kernel separation
Supports 32-bit and 64-bit platforms
Support for ARM, MIPS, PPC, x86
Utilizes the MULTI IDE

## Slide 65: Embedded Linux
Based on the Linux Kernel and used on embedded devices
Supports ARM, MIPS, PPC and x86
No royalties or licensing fees (unless through third parties)
Redistributable source code available
Comparatively larger footprint compared to other RTOS
Familiar OS core and toolchains

## Slide 66: Windows
Graphical operating system made by Microsoft
Introduced in 1985
32bit and 64bit support
Support for x86 and now ARM
Client/Server operating system variants
Various OS SKUs for different purposes

## Slide 67: Windows CE
Windows Embedded Compact Edition
Actually a RTOS as interrupt latency is deterministic
Supports x86 and ARM processors (MIPS prior to version 7)
Optimized version of Windows to run on minimal memory (1MB)
Can be configured to run without volatile storage (ROM)
Larges parts of the Windows CE source is available to OEMs

## Slide 68: Windows IoT
Previously known as Windows Embedded
Includes: Windows NT, XP, 2009, 7 and 8 Embedded
Installation footprint from 40MB (XPE) to 300MB (Win 7 Embedded)
Many embedded SKUs include standard Windows features
Ex. RDP, .NET, Internet Explorer, Media Player may be accessible
IoT Core – Provided for free for hobbyist use

## Slide 69: Windows RT
Mobile Operating System based on the Windows 8 core
Support 32bit ARM processor architecture
Unveiled in 2011 at the Consumer Electronics show
Utilized in Windows tablets
Can only execute software signed by Microsoft

## Slide 70: Tools
Traditional tools are useful in HW reviews
In some cases, specialized tools are needed
Security bits for screws are not unusual
Debugging tools for embedded systems
Hardware tools for chip extraction

## Slide 71: Electrostatic Discharge
Static electricity can fry chips
ESD straps can help minimize ESD
ESD pads for electronic workspaces
ESD equipment not a safety device
Safety procedures must be followed

## Slide 72: Soldering
Process of joining two metal items
Forms a permanent connection (kinda)
Solder melts to join metal (not metals)
Solder is conductive
Breadboard can be used for testing

## Slide 73: Breadboards
Sometimes referred to as prototype board
AKA solderless breadboard
Does not require solder
Reusable across multiple projects
Used for rapid prototyping

## Slide 74: Multimeters
Sometimes referred to as an multi-tester
AKA Volt Ohm Meter
Analog and Digital versions
Usually handheld
Variety of measurements: Current, Volts, amps, ohms

## Slide 75: Capacitors
Used to store electrical energy, acting as a temporary battery
Can be used to block DC while allowing AC to pass
Can be used to filter/stabilize output of power
In some cases used for signal processing
Utilizes color bands for tolerance
Capacitors can have safety risks, handle with care

## Slide 76: Resistors
Used to reduce current
Behavior is defined by Ohm’s law
V = I * R
Can be used in series or parallel
Must be properly rated
Utilizes color codes for rating

## Slide 77: Wires
Used to transmit electricity from a component to another
Must be rated for use (environment, current..etc.)
Size measured in gauge (AWG)
Smaller gauge is a larger wire
Copper, Aluminum, and other metals

## Slide 78: Relays
Electrically operated switch
Can be triggered by applying voltage
Solid state relays
Latching relays
Protective relays

## Slide 79: Variable Power Supplies
Different power requirements for systems
Some require specialized power adapters
VPS provide the correct current/voltage
Usually connects directly to the PCB
DC is commonly used

## Slide 80: Logic Analyzers
Captures digital signals
Attaches to comm bus
Captures signals and records
Decodes common protocols
Can help identify protocols in use

## Slide 81: Rework Stations
Utilize hot air to melt solder points
Air is directed via various nozzles
Temperature can be adjusted
Some include vacuum pumps for cleanup
Many rework stations have soldering iron

## Slide 82: Rework Stations
Rework stations can be very sophisticated
Example: BGA Rework stations
Some rework stations require training
High end rework stations can be expensive
Rework stations can be used to replace chips

## Slide 83: EPROM Programmer
Used to extract firmware directly from chips
Applied correct voltage to correct pins
Adapters can be used for various packages
Can also hook directly to legs
Can be adapted for new chipset
Datasheets are used to create new profiles

## Slide 84: On-chip Debuggers
A mechanism to examine program execution on the target chip
Allows for pausing of program execution (breakpoint)
Allows for the alteration of program values
Increased need for OCD as processors gain speed and complexity

## Slide 85: Bus Pirate
Open source tool that can communicate to hardware interfaces
Allows for JTAG interaction
Allows for FPGA/CPLD programming
Compatible with OpenOCD
Can be slow
May not work with newer chipsets

## Slide 86: J-Link
Made by Segger
One of the most well known debug probes
Supports ARM 7/9/11 and Cortex
Supports Renesas RX
Supports GDB based debugging
Various versions provide different speeds

## Slide 87: Atmel ICE
Debugging tool for Atmel microcontrollers
Supports ARM Cortex-M
Supports Atmel AVR
Provides on-chip debug
JTAG, SWD, TPI
Kit comes with adapters

## Slide 88: Atmel SAM ICE
Debugging tool for Atmel microcontrollers
Supports Atmel SAM microcontrollers
Supports Thumb mode
Provides on-chip debug
JTAG, SWD, SWV
GDB server support

## Slide 89: XILINX
XILINX provides the Vivado IDE for FPGA programming
Supports XILINX hardware debugging devices
eFUSE AES Key/registers
On-chip debug

## Slide 90: Interfacing with Embedded Systems

## Slide 91: Identification

## Slide 92: Datasheets
Datasheet provide tremendous amounts of information about chips
Detailed information on capabilities of microprocessors/controllers
Description of processor architecture
Identification of pinouts and protocols
Identification of support for debugging interfaces
Can greatly aid reverse engineering efforts

## Slide 93: Datasheets

## Slide 94: Datasheets

## Slide 95: Pinouts
Pinout documentation describes the purpose of each pin for a chip
Microprocessors/microcontrollers have over a hundred different pins
Having a reference describing what pins do what is vital to debugging
The sheer number of pins usually make brute force difficult
Utilizing a reference that describes the purpose of each pin is useful
Datasheets usually contain pinout information

## Slide 96: Pinouts

## Slide 97: Pinouts

## Slide 98: Pinouts

## Slide 99: Tracing
Tracing

## Slide 100: JTAGULATOR
Automatic, assisted discovery of on-chip debugging interfaces
Useful when datasheets are not available
Useful when tracing from the processor is not available
Useful when processor pins cannot be reached (ex. BGA)

## Slide 101: Communications Interfaces
Main boards communicate with various components
Systems utilizes various communications interfaces and protocols
Identifying communications interfaces is vital to reverse engineering
Some communications interfaces are custom, but many are standard

## Slide 102: RS-232
RS-232 is very common amongst embedded devices
RS-232 defines the characteristics (voltage, signaling…etc.)
RS-232 also defines interfaces and pin identification
Some vendors have custom interfaces that do not adhere to standard
RS-232 defines the signaling, it does not define the data protocols
Slow, compared to modern standards

## Slide 103: RS-232
Data Carrier Detect
Receive Data
Transmit Data
Data Terminal Ready
Signal Ground
Data Set Ready
Request to Send
Clear to Send
Ring Indicator

## Slide 104: RS-232

## Slide 105: RS-485
RS-485 is very common amongst embedded devices
RS-485 defines the characteristics (voltage, signaling…etc.)
RS-485 also defines interfaces and pin identification
Some vendors have custom interfaces that do not adhere to standard
RS-485 defines the signaling, it does not define the data protocols
Slow, compared to modern standards

## Slide 106: RS-485
D+
Ground
D-

## Slide 107: RS-485

## Slide 108: Transistor-transistor logic
Commonly referred to as TTL
Allows for serial communication
Communication is accomplished by alt between high and low voltage
Common voltages are 5.0V (high) and 3.3V (high) and low
Commonly used for debugging microcontrollers/processors

## Slide 109: UART
Universal Asynchronous Receiver/Transmitter
Used for asynchronous communication
Used to transmits and receive data serially
Transmit one bit at a time at a specified baud rate
9600bps is one of the most common baud rates
Other common baud rates: 19200, 38400, 57600, 115200

## Slide 110: Serial Peripheral Interface Bus
Commonly referred to as SPI
Synchronous serial communications
Used for short distance communications
Typically employs four wire serial-bus
Utilizes a master clock for synchronization
During each SPI clock cycle, full duplex transmission occurs

## Slide 111: Serial Peripheral Interface Bus
SCLK – Serial Clock
MOSI – Master Output Slave Input
MISO – Master Input Slave Output
SDIO – Serial Data I/O
SS – Slave Select

## Slide 112: Inter Integrated Circuit
Commonly referred to as I2C
Pronounced “I” “Two” “C”
Short distance, low speed communications bus
Utilizes 3.3V and 5V for signaling
Utilizes a clock for communications
Master node establishes the clock, slave nodes sync

## Slide 113: Joint Test Action Group (JTAG)
Electronics industry association formed in 1985
Established standards for on-chip debugging and instrumentation
Uses serial communications at different speeds
Some vendors have extended upon the JTAG standard
Applies to many microprocessors/microcontrollers/FPGAs
Different configurations for low pins, regular, and extended

## Slide 114: Joint Test Action Group (JTAG)
TDI – Test Data In
TDO – Test Data Out
TCK – Test Clock
TMS – Test Mode Select
TRST – Test Reset

## Slide 115: Joint Test Action Group (JTAG)
Two pin
  TMSC – Test Serial Data
  TCK – Test Clock

## Slide 116: Serial Wire Debug
Alternative to JTAG
Utilizes a 2-pin electrical interface
Utilizes the same protocol as JTAG
Defined in the ARM debug interface v5
On JTAG devices that support SWD:
  TMS and TCK are used for SWDIO and SWCLK signals

## Slide 117: Reverse Engineering Tools

## Slide 118: Disassembler
Converts machine language into assembly language
Can extract function names and strings
Typically provides call graphs to show code execution flow
Add-ons may be required for embedded processors

## Slide 119: Disassembler

## Slide 120: Disassembler

## Slide 121: Hex Editor
Allows for the manipulation of fundamental binary data
“Hex” stands for hexadecimal

## Slide 122: Cross Compiler
Lab

## Slide 123: Emulators
Lab

## Slide 124: Thanks!
http://whitescope.io
“
Billy.Rios@Whitescope.io
Billy Rios - Founder